GOVERNMENT ENGINEERING COLLEGE, BHUJ

CIVIL ENGINEERING DEPARTMENT

B. E. Sem 5-Civil (2012)

Subject: 150601 - Highway Engineering

| Dt.: 30/08/2012 ASSIGNMENT (Geometric Design) |
| --- |
| Q. 1 | Discuss about the factors which control the geometric elements of highway. |
| Q. 2 | Explain the role of pavement surface characteristics in highway geometric design. |
| Q. 3 | Explain camber. What are the objects of camber? Discuss the factors on which amount of camber depends. |
| Q. 4 | Explain the PIEV theory and derive the expression for SSD at gradient n%. What is ISD? |
| Q. 5 | Explain with sketch the Overtaking Manoeuvre and derive expression for OSD. |
| Q. 6 | What is super-elevation? Derive the necessary expression for highway. |
| Q. 7 | Why extra widening shall be provided on the horizontal curve of highway? Derive its necessary expression. |
| Q. 8 | What is setback distance on the horizontal curve? Describe its design criteria. |
| Q. 9 | Explain with sketches summit curve and valley curve. Discuss their design aspects. |
| Q. 10 | Explain ruling, maximum and exceptional gradients. State the various considerations in deciding the ruling gradient of highway. |

___________

- Copy to Notice Board

(Dr. H. R. Varia)

- P. C. E.

GOVERNMENT ENGINEERING COLLEGE, BHUJ

CIVIL ENGINEERING DEPARTMENT

B. E. Sem 5-Civil (2012)

Subject: 150601 - Highway Engineering

| Dt.: 30/08/2012 TUTORIAL (Geometric Design) |
| --- |
| (1) | Find the SSD for a design speed of 80 kmph. Assume suitable data. What are SSD requirements at a gradient of 1 in 30? |
| (2) | The speed of overtaking and overtaken vehicles are 80 and 60 kmph respectively. If the acceleration of the overtaking vehicle is 2.5 kmph per second, calculate the safe OSD for (i) One way traffic, and (ii) Two way traffic. |
| (3) | Design the rate of superelevation for a horizontal highway curve of radius 300m and speed 80kmph. If the maximum superelevation of 0.07 is not to be exceeded, calculate maximum allowable speed on this curve. |
| (4) | Design following geometric elements on horizontal curve for the ruling design speed of 100kmph. Ruling minimum radius, Super elevation, Extra widening, Length of transition curve, SSD, ISD, and set-back distance. |
| (5) | An ascending gradient of 1:50 meets a descending gradient of 1:80. Determine the length of summit curve to provide ISD and OSD, for a design speed of 80kmph. Assume all other data. |
| (6) | A valley curve is formed by a descending gradient of 1:40 which meets an ascending gradient of 1:30. (i) Design the total length of valley curve if the design speed is 90kmph so as to fulfil both comfort condition and head light sight distance for night driving, after calculating the SSD required. (ii) Find the position of the lowest point of the valley curve to locate a culvert. |

___________

- Copy to Notice Board

(Dr. H. R. Varia)

- P. C. E.

Government Engineering College, Bhuj

Civil Engineering Department

B. E. Semester – 7 Civil - 2012

170604: Urban Transportation System (Department Elective - 1)

Dt: 30/08/2012

Assignment – 3

|  | Trip Distribution Analysis |
| --- | --- |
| Q.1 | Explain briefly various trip distribution methods with their limitations and advantages. |
|  | TUTORIAL: 2 |
| Q.1 | A study area has been divided in four zones 1, 2, 3, 4. the present trip distribution matrix is given with future total trip productions and trip attractions. Develop the future trip distribution matrix using : Uniform growth factor method Average growth factor method Detroit method Fratar method Furness method Do iteration process up to 2 stages wherever possible. D O 1 2 3 4 Total present production Total future production 1 120 150 160 130 560 880 2 140 100 170 120 530 790 3 120 160 150 140 570 820 4 150 170 130 110 560 830 Total present attraction 530 580 610 500 2220 - Total future attraction 800 900 740 880 - 3320 |
| Q.2 | Using a gravity model, with an impedance term of the form C-α, estimate the number of trips from zone – 3 to all other zones. Take α = 1.8 Zone Travel time to zone-3 (min) production Attractions 1 15 20000 10000 2 25 15000 30000 3 - 30000 18000 4 18 25000 10000 5 32 18000 40000 |
| Q.3 | Using gravity model find the no. of trips between zones, show in the following figure. Do iterations up to 3 stages. Assume initially Kij = 1 & α = 2.0. Calibrate the gravity model. |

- Copy to Notice Board

(Dr. H. R. Varia)

A. P. C. E.

# Text boxes

3

2

4

1

6 min

T13 = 100

9 min

T12 = 300

6 min

T24 = 500

9 min

T23 = 300

P1 = 400, A1 = 0

P1 = 0,

A4 = 800

P2 = 800,

A2 = 0

P3 = 0,

A3 = 400